## Slide 1
MSc Advanced Computing · project feasibility · 28 Sep 2026
Does the GPU know what time it is?
Measuring CPU–GPU clock alignment on a laptop, and why the answer points to an OCXO time reference
Pierre · King's College London
Notes: Feasibility experiment run on my own laptop before committing to hardware. Everything in the deck comes from measured data.

## Slide 2
Why a GPU's sense of time matters
±1.5 µs
max time error between 5G TDD base stations (3GPP / ITU-T G.8271)
500 µs
one 5G slot at 30 kHz subcarrier spacing: the deadline the processing must hit
GPU
now runs the radio stack itself (e.g. NVIDIA Aerial), so the GPU's clock sits on the timing path
The question: when code on a GPU reads its clock, how close is that to true time, and how would we even check?
Notes: Timing is the glue of 5G. If AI workloads share the GPU with the radio stack, the GPU's notion of time has to be trustworthy.

## Slide 3
"Synchronise" means two different things
Execution sync
cudaDeviceSynchronize()
"Wait until the GPU has finished." Tells you work is done, not when it finished. The CPU notices late.
Clock alignment
cpu_ns ≈ a · gpu_tick + b
"This GPU timestamp equals that CPU time." Needs offset b, rate a, and an honest error bound. This project is about this one.

## Slide 4
The experiment: bracket every GPU clock read
CPU
GPU
t0: CPU reads TSC,
writes "go"
t1: CPU sees "done",
reads TSC
GPU sees "go", reads its own clock, writes "done"
bracket = t1 − t0: the GPU read happened somewhere inside
Machine
AMD Ryzen AI 7 350 laptop, on battery
GPU
Radeon 860M iGPU (gfx1152), OpenCL 2.0
Clocks compared
CPU TSC ≈ 1996 MHz
GPU REALTIME ≈ 99.81 MHz
Samples
492,400 brackets
Notes: Persistent GPU kernel and CPU thread ping-pong through fine-grained shared memory. No kernel launch inside the loop. GPU clock read via the RDNA 3.5 s_sendmsg_rtn GET_REALTIME message (the AMD equivalent of NVIDIA's %globaltimer).

## Slide 5
Python launch vs native ping-pong
Chart: Bracket width, µs (log scale, lower is better)
| v1 Python, idle | v1 Python, CPU load | v2 native, tight | v2 native, CPU load | v2 native, best 1%
Median bracket (µs) | 840.1 | 232.7 | 28.2 | 55.6 | 1.16
723×
tighter than the first Python attempt (idle median vs native best case)
1.16 µs
best-case bracket: close to the 5G ±1.5 µs budget, but only in the best 1%
Notes: v1: Python launches one kernel per sample and waits, so launch and wake-up overhead swamp everything. v2: a persistent GPU kernel spins on shared memory, compiled C host loop timed with the TSC.

## Slide 6
1
The official clock-pairing API is fake
clGetDeviceAndHostTimer() should return one GPU reading and one CPU reading taken together. On this driver:
device = 12136683975300
host = 12136683975300
Identical. Both are the CPU's performance counter. The GPU clock is never consulted.
Also: kernel start/end timestamps from the driver are already converted into CPU time, with no way to see the conversion. The GPU's real clock (~99.8 MHz) is reachable only through an undocumented instruction (s_sendmsg_rtn GET_REALTIME).
AMD Adrenalin driver 32.0.13070.1002, OpenCL platform AMD-APP 3640.0

## Slide 7
2
On this chip, GPU and CPU clocks are locked
Chart: GPU/CPU rate per 10 s window, parts per billion
| 0s | 10s | 20s | 30s | 40s | 50s | 90s | 100s | 110s | 120s | 130s | 140s | 150s | 160s | 170s | 180s | 190s | 200s | 210s | 220s | 230s | 240s | 250s | 260s
Default run | -2.9 | 11.9 | -9.6 | 10.2 | -15.4 | 2.8 | 13.3 | -12.2 | 0.8 | 8.5 | 21.2 | 4.7 | -10.2 | 4.6 | 0.1 | -1.5 | 10.8 | -6.1 | -7.8 | 3.9 | -3.6 | -0.4 | 7 | -6.8
Tuned run | -4.2 | 4 | 5.2 | -6.9 | 3.3 | 1.9 | 9.9 | -3.2 | 2.6 | 1.2 | -4.6 | 2.1 | -12 | 7.7 | -9.2 | -1.5 | 22 | 0.3 | -2.4 | -10.7 | 5.6 | 4.4 | -1.7 | 11.1
20 : 1
CPU TSC (1996.2 MHz) to GPU clock (99.81 MHz), exact to 0.6 ppb: one shared source
±9 ppb
wander between them: the measurement noise floor, through load, sleep and GPU burn
Notes: The GPU clock runs at 99.81 MHz, not the 100 MHz you'd assume; assuming 100 MHz would be ~1.9 ms wrong per second. But its ratio to the CPU TSC is exactly 20 (within 0.0006 ppm). On an APU both derive from one reference, so relative drift is zero and only latency and offset matter. A discrete NVIDIA card has its own crystal, so there drift is real. That is where the OCXO reference matters most.

## Slide 8
3
Typical round trip is 10–150× the best case
Chart: Median bracket, µs (log)
| Tight loop | Sleepy (~16 ms gaps) | CPU load | GPU load | Tight loop (again)
Default (core 0, normal priority) | 28.2 | 9547.4 | 55.6 | 197.6 | 17.8
Tuned (core 5, time-critical) | 16.3 | 8334.3 | 19.6 | 197.7 | 18.9
Chart: 99th percentile bracket, µs (log)
| Tight loop | Sleepy (~16 ms gaps) | CPU load | GPU load | Tight loop (again)
Default (core 0, normal priority) | 14437.8 | 29353.9 | 29930.3 | 3431.9 | 21543.1
Tuned (core 5, time-critical) | 19888.5 | 28929.1 | 18753.4 | 3169.8 | 25532.9
Tuning (other core, top priority) cuts the median from 56 µs to 20 µs under CPU load, but the millisecond tails stay
Notes: Tight loop: default p50 28 µs, p99 14.4 ms; tuned p50 16 µs, p99 19.9 ms Sleepy (~16 ms gaps): default p50 9.5 ms, p99 29.4 ms; tuned p50 8.3 ms, p99 28.9 ms CPU load: default p50 56 µs, p99 29.9 ms; tuned p50 20 µs, p99 18.8 ms GPU load: default p50 198 µs, p99 3.4 ms; tuned p50 198 µs, p99 3.2 ms Tight loop (again): default p50 18 µs, p99 21.5 ms; tuned p50 19 µs, p99 25.5 ms

## Slide 9
4
Where slow round trips lose their time
Chart: Share of excess time in brackets > 20 µs (default run), %
| Tight loop | Sleepy (~16 ms gaps) | CPU load | GPU load | Tight loop (again)
Before GPU read (GPU slow to notice) | 12 | 99 | 5 | 20 | 2
After GPU read (reply slow to reach CPU) | 88 | 1 | 95 | 80 | 98
54%
of round trips took > 20 µs even in the plain tight loop. The return path dominates, except when the GPU was asleep
39.9 ms
longest single stall. Suspect: the iGPU also drives the display and gets time-sliced (not yet proven)
Notes: Using the fitted clock mapping, each slow bracket can be split into time before the GPU read and time after it. This separates 'GPU was not running our code' from 'CPU was not running our thread'.

## Slide 10
5
Nothing in the machine can referee
CPU and GPU agree perfectly, yet both run 1897 ppm slow against Windows' own timer (QPC). Which is right? Every clock here comes from a cheap crystal on one board, so nothing can referee.
We can measure
the ratio between two clocks, and how tightly a read can be bracketed
We cannot measure
which clock is wrong, or drift that both clocks share (temperature, ageing)
The fix
an external reference ≥10× more stable than either: an oven-controlled crystal (OCXO), disciplined by GPS

## Slide 11
Proposed MSc project: a hardware time referee
GPS antenna
true time, 1 PPS
OCXO board
my PCB (KiCad): 10 MHz + PPS
FPGA PCIe card
counter on OCXO clock, DMA timestamps
Host RAM
"true time = T" updated constantly
CPU + GPU
both read T and their own clock
Research question
How accurately can code on a GPU know true time, and does a PCIe hardware reference beat software CPU–GPU correlation under real load?
Target platform: desktop with NVIDIA RTX (%globaltimer) · GeForce lacks official GPUDirect RDMA, so the card talks to the GPU via host memory

## Slide 12
Plan
1
Done
Software-only feasibility on laptop iGPU: method works, API gap found
2
Next
Port ping-pong to CUDA on a rented RTX; compare with CUPTI's own correlation
3
Build
OCXO + GPS PPS board in KiCad, fab; FPGA counter + DMA (LitePCIe)
4
Test
Idle / load / heat / reference loss; software vs hardware reference vs drift model

## Slide 13
What this does and doesn't show
One laptop, AMD iGPU sharing a clock source with the CPU, on battery. An NVIDIA card over PCIe has its own crystal and will drift.
Bracket midpoints assume symmetric delays; any asymmetry is a hidden constant offset.
Rate stability is relative: shared drift of both clocks is invisible without an external reference.
About 10 minutes of data; thermal and ageing effects need hours.
Takeaway: software alone gets a GPU clock read to ~1.16 µs at best and tens of µs typically, and can't tell which clock is right. A hardware time reference is the missing piece, so it's the thesis.